## Slide 1: 2023 School Expansion
Seventh-day Adventist Church
Tuesday, July 25, 2023
5:00 PM

## Slide 2: Overview
Introductions
About our Project
The Application Process
Exhibits:
  Site Plan
  Landscaping Plan
  Building Elevation
  Photometric Plan
Traffic Impacts
Q&A

## Slide 3: Introduction
Dan Horsch, PE (MN, NC)
  Civil Engineer at SEH – Rochester Office
Paul Armon, AIA
  Architect at Armon Architecture, Inc.

## Slide 4: About our Project
New two-level school with gymnasium
Drop off area
Sidewalk & boulevard trees along 11th Ave NW
Stormwater pond & drainage improvements

## Slide 5: The Application Process
Applicant meets with City Teammates to review application requirements
GET INVOLVED:
Attend Applicant-hosted Neighborhood Information Meeting
Applicant submits Development Application within 30 days of Neighborhood Information Meeting
Full Application Review by City, County, & State departments within 14 days of receiving application
If application meets all requirements, application is approved
Applicant completes other required applications & sign-offs (i.e. building permit, grading permit, etc.)
Applicant proceeds with Project

## Slide 6: Site Plan
Parcel ID: 742214002021
  R-1 Mixed Use Single Family
    Place of Worship
    School
  Lot Area: 153,991 SF (3.54 AC)
Existing Church - 1100 37th St NW
  Gross Building Area: 13,917 SF
Proposed School – TBD 11th Ave NW
  Building Height: 21’-4”
  Gross Building Area: 10,536 SF
  Setbacks
    Front (North): 223 FT (15 FT min.)
    Interior Side (West): 192 FT (5 FT min.)
    Street Side (East): 74 FT (12 FT min.)
    Rear (South): 64 FT (20 FT min.)
  Floor Area Ratio = 0.20 (No Max.)
    Net Buildable Area: 2.87 AC
    Gross Building Area: 0.56 AC
Parking
  Place of Worship: 1 per 5 seats
    350
    Required: 70 spaces
  School: 1 per classroom
    Required: 3
  Total Required: 73 spaces
  Total Provided: 76 spaces

## Slide 7: Landscape Plan
Existing trees are assumed to meet Level 2 Bufferyard requirements
Owner to provide minimal on-site landscaping to match existing church
Boulevard trees every 35’ along 11th Ave NW

## Slide 8: Building Elevation
North
  140’
East
  66’
South
  School – 84’
  Gym – 56’
West
  90’

## Slide 9: Photometric Plan
No parking lot expansion – will use existing site lighting

## Slide 10: Traffic Impacts
Preliminary Trip Generation Analysis
Code 530 – Private School (K-8)
3 Classrooms – 15 students per classroom
  45 students
Estimated additional traffic generated
  185 total daily trips
  45 peak hour (AM) trips

## Slide 11: Q&A

## Slide 12: Still have Questions?
Contact the City of Rochester’s Community Development Department with any questions about this application type via email communitydevelopment@rochestermn.gov or phone (507-328-2600).